Newton’s Method for Approximating Roots

Start with a curve , and select some point  on the curve.  represents our first approximation of a root of the function.

The slope of the tangent line through the point is given by . Plugging into the point-slope form:

1.

2.

The tangent line crosses the x-axis at a point . Plugging this point in for  in Equation 2 above gives us:

3.

Solving for  gives us:

4. , where  is our second approximation for the root of our equation.

By replacing  with  in Equation 4, we get  – our third approximation.

We can continue the process for as long as we need. Normally, we would stop when two successive approximations are identical to a given number of decimal places.

Generalizing the Process

|  | The general formula for the nth approximation is given by . |
| --- | --- |
|  | Evaluate the first derivative of the function, and then plug it and the original function into the general formula. |
|  | For , select an to represent the first approximation. If the function can be expressed as , then find the intersection points. |
|  | Plug the nth approximation into the formula from Step 2 to get the next approximation. |
|  | Repeat Step 4 for , and incrementing n by 1, until , where k represents the number of approximations to be made. |